SpeXman One  SPX01

854X480 PIP FPV Diversity Goggles

Instruction manual

Safety Notice

Warning

- Do Not expose the display area directly in the sun,Optical components will focus the sun,which causes irreversible damage to color liquid crystal display element.This is out of warranty range.

- In order to reduce the damage of fire, electric shock or product hazard, do not expose the SPX01 in the rain and moisture.

- Please use only the recommended accessories.

- Do not disassemble this product,it should be repaired by the professional people.

Caution

- The magnetic field with certain frequency may affect the image and sound of this device.

- DO NOT install or store this device in book cabinet,closet or other closed spaces to avoid such risks as electronic shock,fire and so on due to overheat.

- DO NOT place this device near open fire.

- This device is not dust-proof, waterproof, please note when using.

Package Content

SpeXman One SPX01

2X 5.8G Antenna

2x AV-Out Cable

12V DC-Cable with BEC-Plug

Cable for Futaba RC

Cable for JR RC

Spectacle Case

Cleaning cloth

Function Icons

Operation Instruction

- -Press “MODE” Button to change DIV、AV IN、HDMI IN working Modes.

- -In Div mode，you may firstly enter Menu→General Settings →RF Band，set RF Band to be at the same band with the VTX,then can get receive the video.

- -In MODE setting mode,<MODE>button can choose menu，<OK> button can enter current function setting, <+>button、<->button can adjust value,<MENU> button can return the former layer menu.

DIV Mode

The due antenna diversity receiver is made up of ANT1、ANT2 and receiving circuit,according to their RSSI output,the device can keep receive the strongest signal all the time. and maximize image display stability.

- < - > and < + > button controls the channel change.

- DIV AV OUT outputs diversity receiving signal for video  recorder and external display purposes.

- --DIV AV OUT ONLY works under the diversity mode.

AV IN Mode

- For inputting external video and audio signal.

- In AV IN mode, wireless receiving circuit automatically shut down to save battery life.

HDMI IN Mode

HDMI can input HD video to show much clearer image,and automatically adapt to the resolution (the

maximum input 1920X1080/60Hz)

In HDMI mode,wireless receiving circuit automatically shut down to save battery life.

- -Press the mode button in the HDMI mode, may slow response,waiting for about 11seconds to start HDMI function, this is a normal phenomenon.

Video Setting

Users can change the image display effect by brightness, contrast, saturation, hue, sharpness Settings.

PIP(Picture in Picture) function

Enter Menu→General Settings→PIP，set <PIP>at <ON> to start picture in picture function.

Press<MODE>button to choose<Size>，Press<+>、<->button to choose picture size：420x240pixel、266x160pixel、

133x80pixel;press<MODE>button to choose<Position>，and press<+>、<->button to choose sub-picture's position,8

optional positions,please set it according to your need.

User normal model,long press <OK>button to start or close PIP function.

Foresight camera function

Under DIV、AV IN、HDMI mode,short press<OK>button can fast switch to foresight video to view the surrounding

environment  conveniently.

- -When showing the foresight video,the PIP function will be forced to close,and other functions will stop working either.

- -When switching modes,foresight video will be forced to close.

Operation by RC

Control the foresight video and PIP functions of the unit by PPM signal,firstly enter Menu→System Settings→PPM

Channel，set up PPM channel well，assign one“3”files switch on the RC,for example:H—C（center）L，C—

—C starts PIP or C—L—C(close PIP)，C—H(starts foresight video)，H—C(close foresight video).

Electric Quantity Indication

When using battery for this product,you can choose the corresponding battery serial number：2S、3S、4S、5S、 6S;

when using,it won’t monitor the voltage changing.

-Based on Li battery characteristics to calculate capacity.

Volume

You can change the volume in Menu→General Settings→Volume.

-To avoid too much noise from wireless receiving in the DIV mode, the volume level is not saved, when power

outage, the volume needs to be set again.

Display Scale

Control the input images displayed in a 4:3 or 16:9, work in 16:9 full-screen mode as default.

Menu Display

Can set the icon on the screen to display time and transparency.

Can set menu to display time and transparency.

Reset Menu

Enter reset menu,choose”Yes”, press”OK” to restore all menu items to factory settings.

About Temperature

The product is working with high temperature,this is a normal phenomenon because of the PIP and HDMI functions; the cooling

fans is working as default once the product is powered on,press <MODE> to turn off /on the fan.when the fan is off, the

temperature is hotter,,the built-in fan will starts automatically to release the hot,after the temperature becomes lower,the fan will

be off automatically,you can’t turn off the fan by hands at this situation.

Incons on the Screen

-Different work mode, different icon is displayed on the screen.

-When battery icon showing，it means low battery,please change battery.

Specification

| Display | FOV | : 30 degrees (Diagonal) |
| --- | --- | --- |
|  | Resolution | : 854X480(WVGA) |
|  | Luminance | : 350cd/㎡ |
|  | Interpupillary distance（IPD） | 59.5—69.5mm(adjustable) |
| Wireless Receiver | 5.8GHz ISM frequency | Band | CH 1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 |
|  |  | A | 5865M | 5845M | 5825M | 5805M | 5785M | 5765M | 5745M | 5725M |
|  |  | B | 5733M | 5752M | 5771M | 5790M | 5809M | 5828M | 5847M | 5866M |
|  |  | E | 5705M | 5685M | 5665M | 5645M | 5885M | 5905M | 5925M | 5945M |
|  |  | F | 5740M | 5760M | 5780M | 5800M | 5820M | 5840M | 5860M | 5880M |
|  | Sensitivity | : -90dBm±1dBm |
|  | Channel | : 32Channel ( 4 Band X 8 Channel ) |
|  | Antenna Port | : 2 X SMA,50ohm |
|  | Diversity receiving | : Antenna diversity |
|  | TV System | : NTSC/PAL |
|  | Video output level | : 1.0Vp-p Typ,75ohm |
|  | Audio output level | : 1.0Vp-p Typ,10Kohm |
| Interface | AV IN(Φ3.5,4p) | : Video、Stereo Audio input |
|  | HDMI IN(C Type) | : Support HDMI 1.3 Digital Input, Support HDMI Audio in Support resolution: 1920x1080p50、1920x1080p60、1920x1080i50、 1920x1080i60、1280x720p50、1280x720p60、720x576p50、 720x480p60、720x576i50、720x480i60. |
|  | DIV AV | : Diversity receiving, Video、Audio output |
|  | EAR OUT(Φ3.5,3p) | : Stereo 16Ω/150mW |
|  | PPM IN(Φ3.5,3p) | : Support 8 channel PPM IN |
| Front Camera | FOV | :100 degrees (Diagonal) |
|  | Resolution | :640X480(VGA) |
| Power Supply | DC IN | : 7～28V/ 1A |
|  | Consumption | : 6.8W/12V |
| Dimensions | : 169X70X42mm(not include prominent part) |
| Net Weight | : 182g80Cel 1 |
| Working Temperature | : -10℃～+65℃ |